## Slide 1
Introduction

## Slide 2: Agenda
Teacher introduction
What is the course about
The architecture of wearable IoT systems
Applications of wearable IoT in healthcare and wellbeing
Course program
The exam & The project
Appendix: Data source characteristics

## Slide 3: Who am I
Giacomo Cappon
  Assistant Professor, Department of Information Engineering, University of Padova
  PhD in Information Engineering, curriculum Bioengineering
  Main research interests: signal processing; decision support systems; wearable sensors; digital health; ai for medicine
Contacts
  email: giacomo.cappon@unipd.it
  personal website: https://gcappon.github.io
  public repos: https://github.com/gcappon

## Slide 4: What is the course about?
E-health or digital health: The use of modern Information and Communication Technologies (ICT) to efficiently deliver all kinds of healthcare services
  Examples: EHR, telemedicine systems
Wearables: electronic devices worn close to and/or on the surface of the skin, which detect, analyze and transmit biomedical data, such as heart rate, activity, blood pressure, temperature, etc.
Internet-of-thing (IoT) wearables: Wearables that connect and exchange data with other devices (wearable or not) and systems over the Internet or other communication networks
E-health
Wearables
IoT wearables
Biomedical wearable technologies…

## Slide 5: What is the course about?
Our society is facing some important global health challenges
  Lifestyle-related illnesses driven by sedentary life, consumption of processed and fast foods, alcohol drinking and smoking
    Need to change the paradigm of healthcare, from a mostly reactive system to a proactive system
  Population ageing rises the demand of health services and the healthcare expenditure.
    Need to decentralizing the healthcare
    Covid-19 pandemic called for urgent delivery of healthcare at home
… for healthcare and wellbeing
Biomedical wearable technologies are fundamental to make healthcare scalable and accessible outside the hospital setting and deliver personalized and preventive health services

## Slide 6: Towards a new model of healthcare
Traditional healthcare system:
  Reactive: focused on treating
  Centralized: healthcare at hospitals
  Population-based: maximizing health outcomes of a certain population
  Doctor-centric: only doctor responsible for the patient's care
Biomedical wearable technologies play an important role in realizing a new model of healthcare which is:
  Decentralized: healthcare at home to reduce pressure on hospitals
  Proactive: focused on prevention
  Personalized: maximising the health outcomes of single individuals
  Participatory: engaging individuals in the healthcare process
  Sustainable: better management of resources, patient prioritization

## Slide 7: Examples of biomedical wearable technologies Heart rate monitor
Heart rate (HR): frequency of heart beats [beats/min]
Monitoring HR allows to detect bradycardia (slow HR), tachycardia (fast HR) or arrhythmia (irregular HR)
In hospital:
Electrocardiogram (ECG): electrical activity of the heart measured by on skin electrodes (usually 12)
HR determined as the frequency of peaks of the R wave

## Slide 8: Examples of biomedical wearable technologies Heart rate monitor
Smartwatches use an optical sensor that shines light and measures changes in light absorpion to estimate changes in capillary blood volume
Resulting signal: photoplethysmogram (PPG)
HR estimated as the frequency of P waves
Wearable HR monitors for home use:
Holter monitor: portable ECG monitor, 5 electrodes placed on the chest
Used for medical purpose
Low portability, used for 24-72 hours
Chest straps: electrical activity of the heart measured with electrodes integrated in a chest band/strap

## Slide 9: Examples of biomedical wearable technologies Glucose monitoring sensors
Blood glucose (BG) concentration: concentration of glucose in the blood [mg/dL or mmol/L]
Abnormal BG levels, e.g., hyperglycemia (too high BG) and hypoglycemia (too low BG), may occur in people with metabolism disorders (e.g., diabetes).
In hospital/laboratory:
Biochemistry analyzers
  Exploit a chemical reaction driven by specific enzymes (e.g., glucose-oxidase)
  Invasive (blood sample required), only sparse measurements possible
At home:
Self-monitoring of blood glucose (SMBG) or glucometer:
  drop of capillary blood collected by fingerprick and put in a test strip
  a portable glucose analyzer, through an electrochemical sensor, detects the BG concentration in the capillary blood
  Minimally-invasive but not wearable: only sparse measurements possible (e.g., 3-4 per day)

## Slide 10: Examples of biomedical wearable technologies Glucose monitoring sensors
Continuous glucose monitoring (CGM) sensors
  Minimally-invasive sensors measuring glucose concentration in the interstitial fluid at almost continuous time (e.g., every 5 min) for several consecutive days (e.g., 10 days)
  Needle electrode placed under the skin, exploiting glucose oxidation reaction
  The transmitter, placed over the electrode, wirelessly transfers the measured data to a portable display device
  Mainly used in people with type 1 diabetes

## Slide 11: Modern wearable technologies become IoT
Modern wearable sensors can wirelessly connect to internet-connected devices, such as smartphones, by which the user can share their data with other people (e.g., doctor or family/friends) and upload them in the cloud

## Slide 12: The architecture of wearable IoT systems
1. Sensing layer
2. Network layer
3. Data storing and processing layer
4. Application layer
Alerts
Decision-support
Event log
Self-management
Data analyses
Modeling
Signal processing
Gateway device
WiFi,
Router
Internet
Sensors
Activity tracker
Blood pressure sensor
ECG sensor
Glucose sensor
GSM
Database

## Slide 13: 1. Sensing layer
This layer includes sensors, which are responsible for:
  Collecting the data either directly from the body through contact sensors or from peripheral sensors providing indirect information of body and behaviours
  Preparing the data for on-board analysis, closed-loop feedback or remote transmission for more comprehensive analysis and storing
ECG sensor
Glucose sensor
Contact sensors
Peripheral sensors
Step counter
Microphone and camera
Key components of IoT wearable sensors:
  Miniaturized sensor hardware
  Embedded processor with storage capabilities, power management and communication circuits
Typically limited computing power and storage capabilities.

## Slide 14: 2. Network layer
Fore more comprehensive data analysis and storage, the sensor layer need to transmit the data to cloud computing servers (remotely-located computing machines).
This transmission can be mediated by a companion device that serves as a gateway, i.e., it enables the information to flow from sensors to the cloud server.
  Example of gateway devices: smartphones, tablets and PCs.
The communication must be secured through:
    Authentication protocols for writing, modifying and accessing the data
    Security and privacy protocols for preserving the data
Sensor
Gateway device
Cloud server
Bluetooth
WiFi
GSM

## Slide 15: 3. Data storing and processing layer
Layer responsible for data storing and complex processing
Key components:
  Database for structured data storing
    Data organized based on a specific data model (relational, hierarchical, object-oriented,…)
  Algorithms for data processing
    Statistical analysis
    Feature extraction (e.g., heart rate, calories expenditure, …)
    Signal processing (e.g., filtering, artifact removal, …)
    Data mining (e.g., cluster analysis, anomaly detection, sequential pattern extraction, …)
    Data modeling (knowledge-based, data-driven or hybrid approaches)
    Artificial intelligence (knowledge representation, machine learning, natural language processing, machine perception, automated planning, …)

## Slide 16: 3. Data storing and processing layer
Layer responsible for data storing and complex processing
Key components:
  Database for structured data storing
    Data organized based on a specific data model (relational, hierarchical, object-oriented,…)
  Algorithms for data processing
    Statistical analysis
    Feature extraction (e.g., heart rate, calories expenditure, …)
    Signal processing (e.g., filtering, artifact removal, …)
    Data mining (e.g., cluster analysis, anomaly detection, sequential pattern extraction, …)
    Data modeling (knowledge-based, data-driven or hybrid approaches)
    Artificial intelligence (knowledge representation, machine learning, natural language processing, machine perception, automated planning, …)
Topic not covered

## Slide 17: 4. Application layer
Layer responsible for visualizing raw or processed data to end-users and for providing decision support to them through a software application
Possible end-users: patients, physicians, caregivers, analysts, data managers, administrators, etc.
Possible types of applications:
Mobile app
Desktop app
Web app
App installed in a computer. It can work offline.
App that runs on the browser.
Installation not required. Internet access required.
App installed in a mobile device (e.g. smartphone, smartwatch, tablet, etc.)

## Slide 18: Applications of wearable IoT in healthcare and wellbeing
Some health applications:
Telemonitoring and telemedicine in chronic diseases
Investigative monitoring for diagnostic purposes
Sensor-based biomechanical telerehabilitation
Some wellbeing applications:
Sport and fitness sensing
Activity and sleep monitoring
Falls detection

## Slide 19: Telemonitoring and telemedicine in chronic diseases
Chronic diseases:
  Conditions that last 1 year or more and require ongoing medical attention or limit daily activities
  About 70-80% of the entire healthcare expenditure
Telemonitoring: patient’s data collected by sensors are transmitted to the doctor that review the data
Telemedicine: if necessary, the doctor makes decisions regarding the patient’s health state and provides feedback to the patient
Affordable, clinical-grade sensing for home use are required
Telemonitoring and telemedicine can greatly improve chronic disease management
  Reduce visits and their duration
  Early detection and reaction to adverse health events
  Notify caregivers about health changes that may go unreported or unnoticed by the patient but that may represent early warning signs of an impending health event

## Slide 20: Telemonitoring and telemedicine in chronic diseases
Example: Telemonitoring of glucose concentration in people with diabetes
Through a dedicated telemonitoring application, the doctor can remotely review patients data at any time
Continuous data synchronization
Remote monitoring also possible for parents and caregivers

## Slide 21: Investigative monitoring for diagnostic purpose
Monitoring of health parameters in outclinic context, for a limited period of time (e.g., few days) to detect a particular health condition that cannot be observed in clinic, to track the progress of a disease, or to monitor recovery from a specific health event.
Examples:
  Professional CGM sensor: CGM provided to the patient for a short period (e.g., 7 days). Based on the collected data the doctor can adjust/optimize the patient’s therapy.
  Holter and extended-holter systems: monitor HR for limited periods (e.g., 1-7 days) for detection of heart issues, e.g., cardiac arrhythmias
  At-home sleep test for the diagnosis of obstructive sleep apnea (stops in breathing during sleep): monitoring of sleep at home for at least 1 night using wearable sensors provided by the doctor (breathing sensor, effort belt, pulse oximeter, and microphone)

## Slide 22: Sensor-based biomechanical telerehabilitation
Key components:
  Wearable inertial sensors tracking patient’s movement
  Interactive software
    displays personalized rehabilitation exercises
    receives the sensors’ data
    provides the real-time representations of the patient
    provides visual feedback to the patient, e.g. using an avatar
  A platform for clinicians to remotely follow the therapy sessions in real-time or review the data offline
Main application: remote monitoring of patient performance and progress in a rehabilitation programs (e.g., post-stroke, post-fall, or post-surgical operation)

## Slide 23: Sport and fitness sensing
Most common sensors: chest straps, wristbands, footpods and insoles, sensor patches, sensors in sportwear clothing (smart clothing), sensors in sportwear equipement
Real-time monitoring of performance and coaching through portable display devices
Off-line review of sport statistics, on web-based portals
Data sharing and social networking
Gamification of fitness data: gaming features (e.g. fitness challenges) encourage the adoption of fitness technologies.

## Slide 24: Activity and sleep monitoring
Measurements of activity (steps, distance traveled, etc.), calorie balance, sleep quality.
Objectives:
  Encourage movement in sedentary individuals
  Obesity management: monitor an individual’s participation in a weight management program and maintain engagement
  Sleep monitoring by contact sensors (e.g. wristbands) or non-contact sensors (e.g. under-mattress sleep trackers)
Baby sleep monitoring sensors:
Inertial sensors monitor movement of the chest or stomach area
Built-in tactile stimulator triggered if no movement is detected for 15–20 seconds
If no movement detected after use of tactile stimulation, an alert is generated

## Slide 25: Fall detection
Falls-related injuries are the biggest cause of injury-related death in older adults
Fall detection devices:
  Detection device based on inertial sensors worn on the wrist or waist or as a pendant.
  An algorithm analyses movement measurements in real-time and sends an alert to an in-home base station if a fall is detected.
  The in-home base station notifies a call center, which contacts the wearer.
  If an emergency is determined or there is no response, the call center notifies the emergency services and alerts designated caregivers and family.
Also available in smartwatches used for sport sensing

## Slide 26: The architecture of wearable IoT systems
1. Sensing layer
2. Network layer
3. Data storing and processing layer
4. Application layer
Alerts
Decision-support
Event log
Self-management
Data analyses
Modeling
Signal processing
Gateway device
WiFi,
Router
Internet
Sensors
Activity tracker
Blood pressure sensor
ECG sensor
Glucose sensor
GSM
Database
In this course we will go through the four layers of wearable IoT systems starting from the lowest layer.

## Slide 27: Course program
12 theory lectures
  Monday 12:30-14:30, Room 14E (Padiglione 14 – Fiera di Padova)
Contents:
  Wearable sensor technologies
  World wide web, HTTP communication protocol
  The representational state transfer (REST) paradigm
  Application programming interfaces (APIs)
  Elements of criptography
  Authentication protocols
  Regulation for health data management

## Slide 28: Course program
12 laboratory lectures
  Tuesday 14:30-16:30, Rooms Te+Ue (Polo Didattico di Via Gradenigo)
Contents:
  The Git version control system
  Dart programming language and the Flutter framework
  Building mobile/web applications in Flutter
  User Interface design
  Navigation
  State management
  Basic data persistence
  Networking

## Slide 29: Prerequisites & End of class goals
Prerequisites
  Basic:
    Propension for programming
  Preferable:
    Object-oriented programming
End of class goals
  Learn how wearable devices communicates to the end-user
  Design digital solutions to enhance healthcare and well-being
  Develop a fully functioning mobile application

## Slide 30: The exam
Written test: Theory exam
  15 closed questions
  3 open questions
  Duration: ~90 min
  Max vote: 20/30
Project: Development of an application that integrates and elaborates data from a smartwatch. To be done in groups of 3 students.
  Deadline for completion: The project code must be delivered by July 14th 2024, and no later than the day before the project discussion.
  Discussion of the project (in group): day and time to be defined in dedicated
    Window 1: from 01/07/2024 to 19/07/2024
    Window 2: from 19/08/2024 to 20/09/2024
  Duration of the discussion: 45 min (25 min presentation + 20 min Q&A)
  Max vote: 12/30
Final mark: sum of the votes of the written test and the project.
Dates of the written test
First round: 20 Jun 2024, 14:00 (Room Be+Ve)
Second round: 08 Jul 2024, 14:00 (Room Ae+Be)
Third round: 03 Sep 2024, 14:00 (Room De)
Fourth round: 31 Jan 2025, 14:00 (Room De)

## Slide 31: Project: What’s the spirit here
The goal is learning “How to do SOMETHING using wearable devices”
What I DO expect from you
  To use your imagination to create that SOMETHING
  To learn to build something from scratch
  To use code built by others
  To work together
  To use Google and StackOverflow
What I DO NOT expect from you
  To create the new Google
  To reinvent the wheel (copying others code is fine)
  To create extra complicated UI with animations and stuff
  To implement sophisticated design pattern (even if it would be a nice thing to do)

## Slide 32: Project structure
The project consists of building an app for iOS or Android that collects user data from a wearable device through Web APIs, visualizes them, and does some tricks with them.
Core functionalities:
  Correct app flow
  User authentication and management
  Data collection
  Data visualization and presentation
Additional fuctionalities  It’s up to you! Some examples:
  Run some analysis on data and provide suggestions to the user
  Implement some literature algorithm
  …

## Slide 33: Grading
What are the grading criteria
  Compliance to core functionalities
  Originality of the additional feature
  Quality of teamwork
How much these criteria matter?
  Core functionalities: 50%
  Additional app functionalities: 45%
  Quality of teamwork: 5%
Chart: 
| Core functionalities | Additional functionalities | Quality of teamwork
Sales | 50 | 45 | 5

## Slide 34: Choose your target
Your app must represent a solution for the current SDGs (Sustainable Development Goals) targets
SDG are 17 topics representing the current big challenges humanity must face and solve

## Slide 35: Choose your target
These are the target you can choose from (see the elearning page for more details):
  SDG 2: Target 2.2 (By 2030, end all forms of malnutrition, including achieving, by 2025, the internationally agreed targets on stunting and wasting in children under 5 years of age, and address the nutritional needs of adolescent girls, pregnant and lactating women and older persons) – max 4 groups
  SDG 2: Target 2.3 (By 2030, double the agricultural productivity and incomes of small-scale food producers, in particular women, indigenous peoples, family farmers, pastoralists and fishers, including through secure and equal access to land, other productive resources and inputs, knowledge, financial services, markets and opportunities for value addition and non-farm employment) – max 4 groups
  SDG 3: Target 3.4 (By 2030, reduce by one third premature mortality from non-communicable diseases through prevention and treatment and promote mental health and well-being) – max 8 groups
  SDG 3: Target 3.5 (Strengthen the prevention and treatment of substance abuse, including narcotic drug abuse and harmful use of alcohol) – max 8 groups
  SDG 4: Target 4.7 (By 2030, ensure that all learners acquire the knowledge and skills needed to promote sustainable development, including, among others, through education for sustainable development and sustainable lifestyles, human rights, gender equality, promotion of a culture of peace and non-violence, global citizenship and appreciation of cultural diversity and of culture’s contribution to sustainable development) – max 4 groups
  SDG 8: Target 8.9 (By 2030, devise and implement policies to promote sustainable tourism that creates jobs and promotes local culture and products) – max 4 groups

## Slide 36: Data source
Data that you will use are collected by me using a Fitbit Versa 2
Data are available starting from 09/02 and will be collected up to 30/11
The following data “types” are included(see mor details in the Appendix):
  Calories
  Distance
  Exercise sessions
  Heart rate
  Resting heart rate (Estimated)
  Sleep
  Steps
Your project must use at least 1 type of data

## Slide 37: How to get data - The IMPACT backend
Get token (JWT) using credentials
https://impact.dei.unipd.it/bwthw/
Your app
HTTPS requests/responses
(If credentials are ok) Receive token
Ask for specific data using token
(If request is ok) Receive data (JSON format)
You will be provided with credentials (different for each group) and learn how to get data in the next lessons (lab lesson 9 and 10)

## Slide 38: Tutoring activities
Need help? They are here to cover your back with answers and extra tutoring activities
Calendar of the tutoring activities
Luca Cossu
luca.cossu@phd.unipd.it
Michele Atzeni
michele.atzeni@phd.unipd.it
Day | Time | Room | Topic
3/8/24 | 10:30 - 12:30 | Ae | Tutoring 1: Exercises in Dart
3/15/24 | 10:30 - 12:30 | Ae | Tutoring 2: Exercises in Dart
3/22/24 | 10:30 - 12:30 | Ae | Tutoring 3: Sample App Presentation + Setup
4/12/24 | 10:30 - 12:30 | Ae | Tutoring 4: UI + Navigation
4/19/24 | 10:30 - 12:30 | Ae | Tutoring 5: State Management
5/3/24 | 10:30 - 12:30 | Ae | Tutoring 6: SharedPreferences + Authentication
5/10/24 | 10:30 - 12:30 | Ae | Tutoring 7: HTTP Data request
5/17/24 | 10:30 - 12:30 | Ae | Tutoring 8: Algorithm
5/23/24 | 10:30 - 12:30 | Ae | Tutoring 9: Wrapping up
5/28/24 | 14:30 - 16:30 | Te | Tutoring 10: Bonus
To be confirmed

## Slide 39: Discord server
Join the Discord server to get in touch and ask questions
Link: https://discord.gg/j76A3D27bm
New

## Slide 40: Appendix: Data source characteristics

## Slide 41: Focus on data – Calories
Calories: a list with 1 data point exactly every minute
Fields meaning:
  time: timestamp (hh:mm:ss format) of the calory entry
  value: the calories spent during the last 1 minute (rest + active)
[
  {
  "time": "00:00:00",
  "value": "1.29"
  },
  {
  "time": "00:01:00",
  "value": "1.29"
  },
  {
  "time": "00:02:00",
  "value": "1.29"
  },
  {
  "time": "00:03:00",
  "value": "1.55"
  },
  {
  "time": "00:04:00",
  "value": "1.29"
  },
  {
  "time": "00:05:00",
  "value": "1.29"
  },
  {
  "time": "00:06:00",
  "value": "1.29"
  },
  ...
]

## Slide 42: Focus on data – Distance
Distance: a list with 1 data point every minute or more depending on user’s movement
Fields meaning:
  time: timestamp (hh:mm:ss format) of the distance entry
  value: the distance travelled between the last timestamp and now (in cm)
[
{
"time": "00:03:00",
"value": "0"
},
{
"time": "00:50:00",
"value": "0"
},
{
"time": "01:28:00",
"value": "0"
},
{
"time": "01:32:00",
"value": "1440"
},
{
"time": "01:33:00",
"value": "3110"
},
{
"time": "01:34:00",
"value": "0"
},
{
"time": "01:53:00",
"value": "0"
},
{
"time": "03:09:00",
"value": "0"
},
...
]

## Slide 43: Focus on data – Steps
Steps: a list with 1 data point every minute or more depending on user’s movement
Fields meaning:
  time: timestamp (hh:mm:ss format) of the step entry
  value: the number of steps done between the last timestamp and now
Note: there can be days without data
[
{
"time": "00:07:00",
"value": "0"
},
{
"time": "00:10:00",
"value": "0"
},
{
"time": "01:57:00",
"value": "0"
},
{
"time": "02:29:00",
"value": "0"
},
{
"time": "02:40:00",
"value": "0"
},
{
"time": "02:57:00",
"value": "11"
},
{
"time": "02:58:00",
"value": "18"
},
{
"time": "02:59:00",
"value": "0"
}, ...
]

## Slide 44: Heart rate
Heart rate: a list with 1 data point every 5 seconds.
Fields meaning:
  time: timestamp (hh:mm:ss format) of the heart rate entry
  value: the heart rate at the current time (in bpm)
  confidence: a number from 0 to 3 defining how much the reading is reliable (this problably depends on user movement, etc. You can ignore it)
Note: there can be missing values
[
{
"time": "03:10:19",
"value": 58,
"confidence": 1
},
{
"time": "03:10:24",
"value": 54,
"confidence": 3
},
{
"time": "03:10:29",
"value": 52,
"confidence": 3
},
{
"time": "03:10:44",
"value": 52,
"confidence": 3
},
{
"time": "03:10:54",
"value": 53,
"confidence": 3
},
{
"time": "03:11:09",
"value": 54,
"confidence": 3
},
{
"time": "03:11:19",
"value": 53,
"confidence": 3
}, ...
]

## Slide 45: Resting heart rate
Resting heart rate: an entry per day.
Fields meaning:
  time: timestamp (hh:mm:ss format) of the resting heart rate entry (always 00:00:00)
  value: the estimated resting heart rate at the current time (in bpm)
  error: the estimate error (in %) (Can be ignored)
Note: there can be days without data
{
"time": "00:00:00",
"value": 51.35,
"error": 17.86
}

## Slide 46: Exercise
Exercise: a list with 1 entry for each recorded exercise session
Fields meaning:
  activityName: the type of entry (“Corsa”: Run, “Bici”: bike, “Camminata”: Walk)
  averageHeartRate: the average heart rate during the session
  calories: the active calories spent during the session
  distance: the distance covered during the session
  distanceUnit: the unit of the “distance” field
  duration: the total duration of the session (in ms)
  activeDuration: the total active duration of the session (in ms)
  steps: the total number of steps done during the session (if “Corsa” or ”Camminata”)
  logType: how this record was logged (“tracker” or “auto_detected”)
  heartRateZones: a list that summarizes the number of minutes and calories spent in specific heart rate ranges (from min to max)
  speed: the average speed (in km/h)
  vo2max: the estimated running VO2Max (only for “Corsa” activities)
  elevationGain: the elevation gained during the session
  time: the starting time of the session (format hh:mm:ss)
Note: different activity types can have (slightly) different fields
Note: there can be days without data
[
{
"activityName": "Corsa",
"averageHeartRate": 143,
"calories": 727,
"distance": 8.474117,
"distanceUnit": "Kilometer",
"duration": 3.548E+6,
"activeDuration": 3.214E+6,
"steps": 8604,
"logType": "tracker",
"heartRateZones": [
{
"name": "Fuori zona",
"min": 30,
"max": 110,
"minutes": 3,
"caloriesOut": 30.146219999999971
},
{
"name": "Grassi bruciati",
"min": 110,
"max": 137,
"minutes": 8,
"caloriesOut": 97.13782
},
{
"name": "Attivita aerobica",
"min": 137,
"max": 170,
"minutes": 48,
"caloriesOut": 659.73843
},
{
"name": "Picco",
"min": 170,
"max": 220,
"minutes": 0,
"caloriesOut": 0
}
],
"speed": 9.4981754822650917,
"vo2Max": {
"vo2Max": 48.77853
},
"elevationGain": 28.042,
"time": "11:22:43"
},
{
"activityName": "Bici",
"averageHeartRate": 150,
"calories": 3893,
"distance": 140.143695,
"distanceUnit": "Kilometer",
"duration": 2.0901E+7,
"activeDuration": 1.756E+7,
"logType": "tracker",
"heartRateZones": [
{
"name": "Fuori zona",
"min": 30,
"max": 110,
"minutes": 28,
"caloriesOut": 214.83527999999842
},
{
"name": "Grassi bruciati",
"min": 110,
"max": 136,
"minutes": 64,
"caloriesOut": 664.55027999999993
},
{
"name": "Attivita aerobica",
"min": 136,
"max": 170,
"minutes": 232,
"caloriesOut": 3167.1500100000012
},
{
"name": "Picco",
"min": 170,
"max": 220,
"minutes": 24,
"caloriesOut": 377.76059999999995
}
],
"speed": 28.734978587699313,
"elevationGain": 663.55,
"time": "11:03:54"
},...
]

## Slide 47: Sleep
Sleep: a list with 1 entry for each sleep session
Fields meaning:
  dateOfSleep: day associated to the sleep entry (MM-DD format)
  startTime: the starting timestamp of the sleep (MM-DD hh:mm:ss format)
  endTime: the ending timestamp of the sleep (MM-DD hh:mm:ss format)
  duration: the duration of the sleep session (in ms)
  minutesToFallAsleep: the number of minutes spent to fall asleep
  minutesAsleep: the number of minutes asleep during the sleep entry
  minutesAwake: the number of minutes awake during the sleep entry
  minutesAfterWakeup: the number of minutes the user spent in bed after waking up
  efficiency: the estimated sleep efficiency (from 0 to 100)
  logType: how the entry was logged (always “auto_detected”)
  mainSleep: a boolean indicating if the entry corresponds to the main sleep session
  levels: a summary of the sleeping stages (deep/wake/light/rem/restless) during the sleep session
  data: the stage profile of the sleep session. Each entry contains the starting timestamp, the level, and how much it lasted.
Note: there can be days without data
[
{
"dateOfSleep": "02-14",
"startTime": "02-13 22:44:00",
"endTime": "02-14 06:36:30",
"duration": 2.832E+7,
"minutesToFallAsleep": 0,
"minutesAsleep": 429,
"minutesAwake": 43,
"minutesAfterWakeup": 3,
"timeInBed": 472,
"efficiency": 96,
"logType": "auto_detected", ”mainSleep": true,
"levels": {
"summary": {
"deep": {
"count": 5,
"minutes": 106,
"thirtyDayAvgMinutes": 86
},
"wake": {
"count": 34,
"minutes": 43,
"thirtyDayAvgMinutes": 46
},
"light": {
"count": 28,
"minutes": 235,
"thirtyDayAvgMinutes": 281
},
"rem": {
"count": 11,
"minutes": 88,
"thirtyDayAvgMinutes": 101
}
},
"data": [
{
"dateTime": "02-13 22:44:00",
"level": "wake",
"seconds": 30
},
{
"dateTime": "02-13 22:44:30",
"level": "light",
"seconds": 150
},
{
"dateTime": "02-13 22:47:00",
"level": "deep",
"seconds": 1860
}, ... },
...
]